## Slide 1
12 ft. high ,10 ft.& 8 ft. high chain-link fencing
2 7/8 sch 40 end, corner & gate post
2 3/8 sch 40 line post set 10 ft. on center
10 ft. high fencing to receive a middle rail
12 ft. high fencing to receive two evenly spaced middle rails
12 ft. high back-stop fencing two evenly spaced middle rails and bottom rail
Post footings for the above heights of fencing to be 12" in dia. x 36" deep concrete footings
6 ft. high & 4 ft. high chain-link fencing
2 7/8 sch 40 end, corner , & gate post
2 3/8 sch 40 line post set 10 on center
Post footings for the above heights to be 8" in dia. x 36" in deep concrete footings
7 gage coil bottom tension wire to be installed on all fence heights ( 12’ section of back-stop will have bottom rails)
Top rail, bottom and mid rails to be 1 5/8 sch 40 pipe
All materials to be galvanized
Concrete mix. 2500 psi
YV High School JV Baseball Field fencing Specifications
7600 Sage Avenue Yucca Valley ca
92284

## Slide 2
300’
275’
300’
275’
275’
241’
N
S
W
E

## Slide 3
Elevation= 0 ”
Elevation= +0 ”
Elevation= 0 ”
10’
10’ Slope 0” to +76 “
Existing grade = +76”
10’ Slope 0” to +15 “
Existing grade = 0 ”
Existing grade = -33 ”
Existing grade = -15 ”
25’ Slope 0” to tennis courts
N
S
W
E

## Slide 4
229’- 6’ fence
76’- 6’ fence
60’- 12’ Backstop fence
76’- 10’ fence
256’- 10’ fence
178’- 12’ fence
12’ FENCE
8 ’ FENCE
4’ FENCE
6’ FENCE
10’ FENCE
N
S
W
E

## Slide 5
20’
20’
20’
10’
10’
3’X6’
3’
3’
30’
30’
70’
70’
8’
8’
GATE
GATE
3’X6’
3’X6’
3’X6’
N
S
W
E
12’ FENCE
8 ’ FENCE
4’ FENCE
6’ FENCE
10’ FENCE

## Slide 6
282’
12’
12’
6’
6’
10’
10’
N
S
W
E